Overview of Urban Drainage Flood Forecasting Methods and Approaches

J. Chen 1 and B. Adams 2

- Water Survey Division, Environment Canada

- Department of Civil Engineering, University of Toronto

Abstract: Urban drainage hydrological modeling plays a crucial role in planning and design of urban infrastructure towards building a sustainable environment. Nowadays, as a result of intensified economic development and urbanization, numerous new large urban centers continue to emerge and evolve worldwide. The rapid expansion of urban population and the demand for a better quality of life is posing unprecedented stress and challenges on urban environment. Rainfall-runoff modeling is considered as an effective tool for configuration of urban drainage systems, whereas flood forecasting is regarded as an effective measure for mitigating unnecessary economic loss and building sustainable urban infrastructure. For this purpose, hydrological models based on various approaches have been developed to facilitate flood forecasting, flood control and defence. For urban drainage system design, numerous hydrological models are available and these models vary considerably in terms of model structure and capability ranging from the simplest rational method to more sophisticated modeling tools or package such as US EPA storm water management model (SWMM) for comprehensive urban drainage planning and design. However, despite variations in complexity, these models generally fall into three broad categories, i.e., design storm models, derived probability distribution models and simulation models. In this study, various modeling approaches or hydrological models, e.g., rational method, analytical models, simulation models such as OTTHYMO (Canada), HEC-HMS (US) and SWMM (US) were employed for runoff simulation in a test catchment which drains into the Lake of Ontario. The results from different models were compared and evaluated. Conclusions from this study provide valuable insights into flood control and mitigation with stormwater management facilities in the Great Toronto Area.

Key Words: Flood Defence; Urban drainage; Analytical model; Rational method; Simulation model.

# Urban trainage modeling approaches

Hydrological models as an effective tool have been widely applied to the planning and design of urban flood control infrastructure. In terms of modeling approaches, hydrologic modeling generally falls into three broad categories, i.e., design storm approach, derived probability distribution approach and simulation approach which can be further divided into event or continuous simulation based on the time scale employed. While different types of models may vary considerably in terms of the level of complexity, in reality, the three types of models have been effectively used in the configuration of urban drainage system facilities.

Despite its age and simplicity, the rational method is still routinely applied in modeling of urban stormwater runoff, especially for the estimation of peak runoff flow rates. The underlying principle of this method is that the maximum runoff flow rate from a drainage area will occur when the entire area is contributing to runoff. As a result, the peak flow rate is computed directly from a simple product of the runoff coefficient, rainfall intensity and catchment area. For many years, the rational method remains as one of the most simple and popular runoff computation methods for planning and design of urban drainage system (Titmarsh et al., 1995; Singh and Cruise, 1992; Kuichling, 1889). Becciu and Paoletti (2000) proposed a modified form of the rational method taking into account the randomness of the runoff coefficient to achieve a better estimation of design peak flow. Guo (2001) extended the method to generate a complete runoff hydrograph under a continuous nonuniform hyetograph. Hua at al. (2003) showed that an extended rational formula might be applicable to the case where the rainfall duration is less than the basin concentration time.

The design storm approach assumes that the design storm hyetograph itself has some known frequency or return period and that the resulting simulated runoff hydrograph itself has the same known frequency. While patterns of design storms can be easily constructed, and may be standardized for regulatory purposes, this method generally gives conservative estimates of peak flows (Huber, 1993). Marsalek (1984) showed that peak flow rates computed from using Chicago-type design storms were significantly larger than those obtained from historical storms. Adams and Howard (1985) strongly argued against the use of design storms. There are concerns that the fundamental assumptions underling this approach is flawed or meaningless, since it does not account for antecedent soil moisture conditions within the catchment and the potential temporal variation of storm hyetograph patterns. In addition, design storms cannot express the full range of meteorological characteristics encountered by the drainage system. The adequacy of the design storm approach is questionable for the design of both stormwater quantity and quality control facilities, whose long-term performances are more critical than single design event performances (Adams and Papa, 2000). The limitations and drawbacks of design storm approach were also discussed at length by James and Robinson (1986).

Simulation models have been used extensively for flood frequency analysis (Cameron et al., 1999; Blazkova and Beven, 1997; Bradly and Potter, 1992; Bras et al., 1985). Simulation models normally consist of a number of conceptual elements to depict rainfall-runoff physical process such as evaporation and infiltration. This type of models may be further divided into event or continuous simulation models depending on the time scale employed. In flood forecasting, simulation models are frequently employed to predict drainage system response driven by event rainfall or single design storm. In contrast to event simulation models, continuous simulation may take advantages of historical long-term rainfalls that are more widely available and usually have longer periods of records than runoff data, and can be employed as a complement to the regionalized regressions which use catchment characteristics to estimate flood frequencies for an ungauged catchment (Blazkova and Beven, 2002). In North America, it is a common practice to employ event simulation models such as HEC-1 or HEC-HMS (US) and OTTHYMO or Visual OTTHYMO (Canada) to perform hydrological simulation with design storms as inputs. In previous studies, the HEC-1 model was employed in watershed runoff simulation (Duru and Hjelmfelt, 1994; Luce and Cundy, 1992; Dawdy, 1991; Wilcox et al., 1990). Accepted and recommended by the Ontario Ministry of Environment (MOE) and Ministry of Transportation (MTO), the OTTHYMO model as an event simulation model has been applied extensively in consulting engineering across Canada for sizing of urban storm sewers and various Best Management Practices (BMPs).

Application of derived probability distribution approach to water resources engineering was pioneered by Eagleson (1972, 1978). Since then, the derived probability distribution approach has increasingly been employed in flood frequency analysis (Gottschalk and Weingartner, 1998; Cadavid et al., 1991; Diaz-Granados et al., 1984). In urban drainage design, the derived probability distribution approach has long been employed as effective tools for sizing stormwater facilities and evaluating system performance (Li and Adams, 2000; Guo and Adams, 1998; Segarra-Garcia and Loganathan, 1992; Loganathan et al., 1985; Loganathan and Delleur, 1984; DiToro and Small, 1979; Small and Ditoro, 1979; Howard, 1976). Various studies showed that the closed-form analytical models are able to generate comparable results to continuous SWMM simulation results (Chen and Adams, 2006; 2005; Chen, 2003; Guo and Adams, 1998). In the evaluation of different types of models, Nnadi et al. (1999) compared design storm concepts using continuous simulation with short duration storms. The sensitivity and reliability of urban design storm was evaluated by continuous simulation (Voorhees and Wenzel, 1984). The influence of storm temporal patterns on catchment response was investigated by Ball (1994). Guo (2001) examined the Rational Method under the 6-h SCS design rainfall distribution for small urban catchment and concluded that rational method provided good agreement to those obtained from HEC-1 model.

In terms of various modeling approaches, the emphasis of this study is to evaluate different types of models including the simple rational method, simulation models and analytical models developed with derived probability distribution theory. In particular, the performance of the commonly used event simulation models (i.e., HEC-HMS and Visual OTTHYMO) are assessed against continuous simulation model (i.e., SWMM), whereas the applicability of analytical models as an alternative to simulation models for planning and design of flood control system is evaluated by comparing the model performance with rational method as well as those event or continuous simulation models.

# Urban trainage Flood frequency analysis with analytical models

Since simulation models such as SWMM, HEC-HMS and Visual OTTHYMO are well known, some background associated with application of these models are well documented and therefore omitted here. This section is mainly devoted to the introduction of analytical models for urban drainage flood control analysis. The fundamental in the development of analytical models is derived probability distribution theory and the key element is rainfall-runoff transformation, based on which the probability distributions of rainfall characteristics, such as rainfall volume, duration and interevent time, are mathematically transformed by hydrologic and hydraulic relationships to create probability distributions of system outputs. While this type of models is usually intended for preliminary or screening-level urban drainage system planning and design, they can provide closed-form solutions describing the complete probability distributions of system performance parameters.

The integrated analytical model proposed in this study as shown in Figure 1 consists of a number of functional components, such as rainfall-runoff transformation, pollutant buildup, washoff, stormwater runoff control in storage/treatment facility, etc. The development of each component is guided by a number of methodological considerations. For example, the rainfall-runoff transformation which actually conceptualizes the major runoff generation mechanisms in the drainage area can be formulated with a runoff coefficient approach as follows (Chen and Adams, 2005):

(1)

where  is the impervious area depression storage,  is the pervious area depression storage,  is the pervious area runoff coefficient, and h is the fraction of impervious area of the urban catchment. Based on the transformation, the probability density function (PDF) of runoff volume can be derived as follows:

Figure 1: Urban Drainage Flood Control Analysis with Analytical Models

(2)

where  equals inverse of the average rainfall event volume.

The cumulative distribution function (CDF) of the runoff volume can be derived from the PDF of runoff volume. Further more, based on the rainfall-runoff transformation, system performance measures, such as the average annual volume of spills, runoff quantity capture efficiency, the fraction of pollutant removed in the storage/treatment facilities as well as long term pollutant load to receiving waters can be derived and evaluated (Chen and Adams, 2005; 2006; Chen, 2003). With the development of the integrated analytical models, the existing drainage systems can be operated and yet-to-be-built systems can be designed to achieve both required levels of quantity and quality control.

# Discussion of results

The case study is based on the drainage area located in the Great Toronto Area under Stormwater Assessment Monitoring and Performance (SWAMP) Program, Performance Assessment of a Stormwater Retrofit Pond - Harding Park, Richmond Hill, Ontario (2002). To evaluate different types of simulation models, and the applicability of analytical models for flood frequency analysis, the estimated peak flow rates with analytical models were plotted along with continuous SWMM simulation results in Figure 2. To facilitate the comparison, the estimated runoff volumes based on analytical models were also plotted along with continuous SWMM simulation results in Figure 3. From Figure 2, it appears that peak flow rates from analytical model are comparable with continuous simulation results. Nevertheless, analytical model is likely to overestimate flood quantiles with a relatively low magnitude or return period, and underestimate flood quantiles with a relatively high magnitude or return period. By comparison, Figure 3 indicates that analytical model is able to provide good estimates of runoff volume for those runoff events with a relatively low flow rate or return period.

Figure 2. Comparison of Peak Flow Rates from analytical model and SWMM

Figure 3. Comparison of Runoff Volumes from analytical model and SWMM

With the 4-hour Chicago type of storm as input, a comparison of the estimated peak flows from different models is illustrated in Figure 4. As shown in the figure, the Visual OTTHYMO model tends to generate the highest peak flow rates compared with the results from other models. The peak flow rates from rational method are obviously lower than the estimates from Visual OTTHYMO model. The event SWMM simulation model is able to generate peak flow rates in between of the results from the Visual OTTHYMO model and rational method. By comparison, the HEC-HMS tends to produce the lowest estimates of peak flows. The figure also shows that the peak flows generated by continuous SWMM simulation are significantly lower than the results from event simulation, and the analytical model results are clearly in a better agreement with continuous SWMM simulation results.

Figure 4. Comparison of Peak Flow rates

Figure 5. Comparison of Runoff Volumes

Figure 5 shows a comparison of the estimated runoff volumes based on various models. With reference to Figure 4, it was noted that the highest runoff volume curve was not generated by Visual OTTHYMO model which tends to generate the highest peak flow rates (in Figure 4), the highest runoff volume curve was generated by continuous SWMM simulation model, whereas the runoff volumes from event SWMM simulation appear to be lower than both continuous simulation and Visual OTTHYMO model results.  Also shown in the figure, the lowest curve was produced by rational method. By comparison, analytical model is capable of generating more comparable results to those from event SWMM simulation results. HEC-HMS model is able to produce runoff volumes in between of the results from analytical model and rational method. Considering that the results from continuous simulation are normally deemed more reliable, the event simulation models (Visual OTTHYMO, HEC-HMS and SWMM), analytical models and rational method are likely to underestimate runoff volumes. The potential implication is that urban drainage flood control systems are more likely undersized based on event simulation models.

# Conclusions

This study attempts to paint a big picture regarding the applications of different types of hydrological models. In terms of model performance, the Visual OTTHYMO model appears to generate the highest peak flows compared with other event simulation models, whereas HEC-HMS tends to significantly underestimate peak flows. In contrast, the closed-form analytical model is capable of generating comparable results to continuous SWMM simulation results in terms of either peak flow rates or runoff volumes. While different models may have their advantages and disadvantages, for urban drainage system design including the sizing of flood control facilities, analytical models can be employed as an alternative to continuous simulation models.

# References

Adams, B. J., and Howard, C. D. D.1985. The Pathology of Design Storms. Publication 85-03, University of Toronto, Department of Civil Engineering, Toronto, Ontario.

Adams, B. J., and Papa, F. 2000.  Urban Stormwater Management Planning with Analytical Probabilistic Models, John Wiley and Sons, New York, NY.

Ball, J. E. 1994. The influence of storm temporal patterns on catchment response. J. Hydrol., 158(3-4), 285-303.

Becciu, G., and Paoletti, A. 2000. Moments of runoff coefficient and peak discharge estimation in urban catchments. J. Hydrol. Engrg., ASCE, 5(2), 197205-70.

Blazkova, S., and Beven, K. 2002. Flood frequency estimation by continuous simulation for a catchment treated as ungauged (with uncertainty), Water Resour. Res., 38(8), 14-1.

Blazkova, S., and Beven, K. 1997. Flood frequency prediction for data limited catchments in Czech Republic using a statistic rainfall model and Top Model, J. Hydrol., 195, 256-278.

Bradly, A.A., and Potter, K.W. 1992. Flood frequency analysis of simulated floods. Water Resour. Res., 28, 2375-2385.

Bras, R.L., Gaboury, D.R., Grossman, D.S., and Vicen, G.J. 1985. Spatially varying rainfall and flood risk analysis. J. Hydrologic Engrg., 3, 754-773.

Cadavid, L., Obeysekera, J. T. B., Shen, H. W. 1991.  Flood frequency derivation from kinematic wave, J. Hydrol. Engng., 117(4), 489-510.

Cameron, D. S., Beven, K. J., Tawn, J., Blazkova, S., and Naden, P. 1999. Flood frequency estimation by continuous simulation for a gauged upland catchment (with uncertainty). J. Hydrol., 219(3-4),169-187.

Chen, J.Y. and Adams, B.J. 2006. Urban Stormwater Quality Model Based on Pollutant Buildup and Washoff Processes. Journal of Environmental Engineering, ASCE, 132 (10).

Chen, J.Y. and Adams, B.J. 2005. Urban Stormwater Control Evaluation with Analytical Probabilistic Models. Journal of Water Resources Planning and Management, ASCE, 131(5).

Chen, J. Y. 2003. Integrated Urban Stormwater Management Modeling, Ph.D. dissertation, Department of Civil Engineering, University of Toronto, Toronto, Ontario, Canada.

Dawdy, D.R. 1991. Comparison of USGS and HEC-1 kinematic wave runoff models. In: Recent Advances in Modeling of Hydrologic Systems, S. Bowles and P.E. O’Connell (eds.). Kluwer Academic, Dordrecht, 549-557.

DiToro, D. M., and Small, M. J.1979. Stormwater interception and storage. Journal of Environmental Engineering, ASCE, 105(EE1), 43-54.

Duru, J. O., and Hjelmfelt, A. T.  Jr. 1994. Investigating prediction capability of HEC-1 and KINEROS kinematic wave runoff models. J. Hydrol., 157(1-4), 87-103.

Diaz-Granados, M. A., Valdes, J. B., and Bras, R. L.1984. A physically-based flood frequency distribution. Water Resour. Res., 20(7), 995-1003.

Eagleson, P. S.1972. Dynamics of flood frequency. Water Resour. Res., 8(4), 878-897.

Eagleson, P. S. 1978. Climate, soil, and vegetation 2, the distribution of annual precipitation derived from observed storm sequences. Water Resour. Res., 14(5), 713-721.

Gottschalk, L., and Weingartner, R. 1998. Distribution of peak flow derived from a distribution of rainfall volume and runoff coefficient, and a unit hydrograph. J. Hydrol., 208, 148-162.

Guo, C.Y. 2001. Rational Hydrograph Method for Small Urban Watersheds. J. Hydrol. Engrg., 6(4), 352-356.

Guo, Y., and Adams, B. J. 1998. Hydrologic analysis of urban catchments with event-based probabilistic models, 1. runoff volume. Water Resour. Res., 34 (12), 3421-3431.

Guo, Y., and Adams, B. J. 1998. Hydrologic analysis of urban catchments with event-based probabilistic models. 2. peak discharge rate.Water Resour. Res., 34 (12), 3433-3443.

Howard, C. D. D. 1976. Theory of storage and treatment plant overflows, J. Environ. Eng., ASCE, 102(EE4), 709-722.

Hua, J., Liang Z, and Yu, Z. 2003. A modified rational formula for flood design in small basins. Journal of the American Water Resources Association, 39 (5), 1017-1025.

Huber, W. C. 1993, Comparison between design storm and historical storm approaches for urban drainage design. In: Urban Storm Drainage, Proceedings, U.S.-Italy Bilateral Seminar, C. Cao, B. C. Yen, and M. Benedini (eds.), Water Resources Publication, 81-90.

James, W., and Robinson, M.1986. Continuous deterministic urban runoff modeling. In: Urban Drainage Modeling, Proceedings of the International Symposium on Comparison of Urban Drainage Models with Real Catchments Data, UDM’86 Dubrovnik, Yugoslavia. C. Maksimovic and M. Radojkovic (eds.), Pergamon Press, 347-378, 1986.

Kuichling, E.1889. The relation between rainfall and the discharge of sewers in populous districts. Trans., ASCE, 20, 1-56.

Li, J.Y., and Adams, B. J. 2000. Probabilistic models for analysis of urban runoff control system, J. Environ. Eng., ASCE, 126 (3), 217-224.

Loganathan, G. V., and Delleur, J. W.1984. Effects of urbanization on frequencies of overflows and pollutant loadings from storm sewer overflows: a derived distribution approach. Water Resour. Res., 20(7), 857-865.

Loganathan, G. V., Delleur, J. W., and Segarra, R. I.1985. Planning detention storage for stormwater management. J. Water Resour. Plng. and Mgmt., ASCE, 111(4), 382-398.

Lucy, C.H., and Cundy, T.W.1992. Modification of the kinematic wave-Philip infiltration overland flow model. Water Resour. Res., 28(4): 1179-1186.

Marsalek, J. 1984. Urban runoff peak frequency curves. Nordic Hydrology, 15 (85-102).

Nix, S. J. 1994, Urban Stormwater Modeling and Simulation. Lewis Publishers, Boca Raton, FL.

Nnadi, F. N., Kline, F. X., Wray, H. L. Jr., and Wanielista, M. P.1999. Comparison of design storm concepts using continuous simulation with short duration storms. Journal of the American Water Resources Association, 35 (1), 61-72.

Segarra-Garcia, R., and Loganathan, V. G. 1992. Stormwater detention storage design under random pollutant loading. J. Water Resour. Plng. and Mgmt., ASCE, 118(5), 475-491.

Singh, V. P., and Cruise, J.F. 1992. Analysis of the rational formula using a system approach. Catchment runoff and rational formula, B.C. Yen, ed., Water Resources Publication, Littleton, Colo., 39-51.

Stormwater Assessment Monitoring and Performance (SWAMP) Program, Performance Assessment of a Stormwater Retrofit Pond - Harding Park, Richmond Hill, Ontario, Toronto and Region Conservation Authority, 2002.

Titmarsh, G.W., Cordery, I., and Pilgrim, D.H.1995. Calibration procedures for the rational and USSCS design flood methods. J. Hydrol. Engrg., ASCE, 121(1), 61-70.

Voorhees, M. L., and Wenzel, H.G. Jr. 1984. Urban design-storm sensitivity and reliability. J. Hydrol., 68(1-4), 39-60.

Wilcox, B.P., Rawls, W.J., Brakensiek, D.L., and Wight, J.R. 1990. Predicting runoff from rangeland catchments: a comparison of two models. Water Resour. Res., 26(10): 2401-2410.